## Slide 1: 2012 Wireless Microtel Inn & Suites 612 Nikles Street Bozeman, MT 59715

## Slide 2
Issues Reported
Some users are reporting no internet after connecting to an Access Point.
Employees are not sure what to reset to restore Internet back to their clients.
Employees and previous contractors have not been able to locate Access Points.
Causes Found
Several network connections were found loose or not plugged in properly.
No network map has been put together for this site.
There is no centralized management and diagnostics station for this site.
No captive portal with an access agreement
Access Points are named “mtl25900n” (where n is a number from 1-4). This naming is confusing to clients, who may accidentally connect to a neighboring access point.
Resolutions
Corrected loose network connections and verified connectivity.
Tested each access point and found a week one that needs replacing.
Located and mapped all four Access Points.
Cisco switch is not capable of producing 802.3af PoE.