## Slide 1: HFI Astrometry: requirements and problems
Scientific Requirements
  Relative pointing error: < 1/5 beam = 1
    Needed for averaging over ring
  Attitude measurement error: < 9
    Needed for minimizing effective beam-smearing
    Beam smearing < noise at l1600

## Slide 2: Astrometry
Once
  Initial pointing (may be off by 1°)
Slowly-varying
  Boresight angle
  Rotation of focal plane
  Detector angles within focal plane
Each circle
  Mean spin-axis position
  Nutation around spin axis
  Spin velocity, phase

## Slide 3: Astrometry: Specific Issues
Initial pointing:
  Bright sources (incl. Galactic plane) in first ~day’s data (“manual” fix?)
Boresight angle, detector positions
  Known, bright sources.
  Compile statistics on detected known sources
Need to check accuracy of star tracker
  including nutation
Star tracker backup?

## Slide 4: Astrometry: Specific Issues (II)
Nutation from flight data?
  Map-making and harmonic both require nutation amplitude has negligible effect on beam:
    Amplitude <1or solution <<1
  Not enough bright sources for nutation solution on each ring (see DH presentation)
Polarized channels?
LFI?

## Slide 5: Documents
Pointing WT: Objectives and Plan (Maino, Van Leeuwen)
Position and Orientation of HFI Horns (11 Jun ‘01)
Pointing Accuracy: HFI Scientific Requirements and HFI Provided Measurements (Puget, Lamarre, Sygnet)
Pointing Accuracy: Scientific Requirements and Implementation (Puget, Lamarre, Sygnet, Hivon)