## Slide 1: CAN Bus Access and Arbitration: How it works Important: Identifiers are unique!
Node X
Node A
Node B
Node C
Transmit Request
Remainder
Node A
Node B
Node C
Arbitration phase
CAN Bus
Start Bit
Node B loses Arbitration
Node C loses Arbitration
Identifier Field
Notes: <number>
<footer>
<header>
<date/time>
The arbitration concept avoids collisions of messages whose transmission was started by more than one node simultaneously and makes sure the most important message is sent first without time loss. In the picture above you see the trace of the transmit pins of three bus nodes called A, B and C, and the resulting bus state according to the wired-AND principle.
If two or more bus nodes start their transmission at the same time after having found the bus to be idle, collision of the messages is avoided by bitwise arbitration. Each node sends the bits of its message identifier and monitors the bus level.
At a certain time nodes A and C send a dominant identifier bit. Node B sends a recessive identifier bit but reads back a dominant one. Node B loses bus arbitration and switches to receive mode. Some bits later node C loses arbitration against node A. This means that the message identifier of node A has a lower binary value and therefore a higher priority than the messages of nodes B and C. In this way, the bus node with the highest priority message wins arbitration without losing time by having to repeat the message.
Nodes B and C automatically try to repeat their transmission once the bus returns to the idle state. Node B loses against node C, so the message of node C is transmitted next, followed by node B’s message.
It is not permitted for different nodes to send messages with the same identifier as arbitration could fail leading to collisions and errors.