## Slide 1: IEEE MVEDR P1616: Data Definition Sub Working Group Report: September P1616 Meeting (9/23/2002)
Data Definition SWG
Hideki Hada
Tel: 734-973-4432, Fax: 734-973-4470, Cell: 734-649-7645, hhada@aol.com

## Slide 2: Contents
DD SWG Member List
DD SWG Documents
Reminder
Scope
Purpose
Objectives
Deliverables
Background
Timeline
  Short-Term (Sept. 23, 2002)
  Mid-Term (starting Dec., 2002)
  Long-Term (2003)
Methods and Materials
Objectives vs. SWG Products
  Existing Data Definitions
    IEEE SCC12 ITS
    SAE J1939
    NHTSA EDR WG
  Selection of Data Elements
  Data Attributes
    ITS Data Registry
    Language
Reference
Check List
Assignments
Goals of Sept. 23-24 meeting:
  Obtain P1616 approvals for the Charter of DD SWG.
    Scope, Purpose, Deliverables, Schedule
  Choose methods to select:
    Data elements and attributes
  Define the way to finalize the format of EDR data definition.
  Select several data elements to develop examples of EDR data definition.
  Clearly defines the work to be done before Dec. P1616 meeting.

## Slide 3: DD SWG Member List (9/23/2002)
File: DD SWG Member List.doc

## Slide 4: DD SWG Documents
Data Definition Sub Working Group Member List
  DD SWG Member List.doc
WORK PLAN (DRAFT #2) for IEEE P1616 Sub Work Group for Data Definitions
  p1616SWGforData-WorkPlan-draft2.doc
Example of Data Definition from ITS Data Registry
  Sample from ITS Data Registry.doc
Event Data Recorders: Link with Accident Database,
  IEEE_DatabaseLink.ppt
Data Elements Characterization Methodology
  IEEE_DataElementCharacterizationMethodology.doc
Fatality Analysis reporting System: Data Element Classification
  IEEE_FARS_Elements_classification.xls
IEEE SCC32 – Standard Coordinating Committee on Intelligent Transportation Systems (ITS)
  SCC32ITS.doc
IEEE Intelligent transportation Systems Data Registry
  ITSdataRegistry.doc
Event Data Recorders, Summary of Findings by the NHTSA EDR Working Group Volume II, Supplemental Findings for Trucks, Motorcoaches, and School Buses – Extraction of Data Elements
  T&BEDRDataElements.xls
Examples of Data Definition - Administrative Meta Attributes
  Metaattributes.xls
MVEDR Data Definition SWG Teleconference Memo (9/13/2002)
  dd swg telecon 091302

## Slide 5: Reminder – Architecture
This area is NOT the work of DD SWG.
Data definition internal to EDR & vehicle systems.
Method of data collection, storage and extraction.
Method of data conversion during data extraction.
Method of data sharing among data users/sources.
The work area of DD SWG is:
Data definition of EDR-related data after extracted from EDRs so that various users can compare and/or integrate data from different sources for their unique purpose.
ECU-1
ECU-2
ECU-4
ECU-3
Sensors
Sensors
EDR
Data
Data
Data
Data
Data
Common Connector
Common Data Extraction Protocol
Vehicle Bus
Vehicle
Vehicle A
Vehicle B
Vehicle C
Data Sources
A-C-N and
Medical Users
Transportation
Infrastructure
Accident Database
Vehicle and Device
Manufacturers
Service Industry
Data Users
Transportation/Communication Infrastructure
EDR Data in a Common Data Format

## Slide 6: Reminder – Communication
DD SWG develops a common data definition from the view point of data users (not from the one of communication device design).
Layer 7: Application
Layer 6: Presentation
Layer 5: Session
Layer 4: Transport
Layer 3: Network
Layer 2: Data Link
Layer 1: Physical
Data
ISO / OSI 7-Layer Model
This is our work area.
Transforms file messages
Handles file format differences
Provides synchronization of data flow
Provides end to end delivery
Switches and routes information (router)
Delivers information to the next nodes
Transmits bit stream on physical medium
Speed:
47km/h
V=47km/h
01010011
01010011
01010011
01010011

## Slide 7: Scope
This subgroup will
  1) define a set of data elements for inclusion in the data dictionary and
  2) develop specifications for each data element.
Specifications will consist of descriptive attributes, such as full-scale range, resolution, sampling rate, and units. To the extent possible, the group will make use of and attempt to be compatible with other standards bodies working on similar data definitions. The group may define specific data sets for different classes of vehicles.
It should be noted that the selection of particular data elements for inclusion in the data dictionary is determined by consensus of the P1616 Committee. Inclusion or exclusion of particular data elements from any version of this standard does not reflect prioritization. This standard will be updated periodically, and new data elements will be added/deleted, as appropriate.
File: p1616SWGforData-WorkPlan-draft2.doc

## Slide 8: Purpose
Many light-duty motor vehicles, and increasing numbers of heavy commercial vehicles, are equipped with some form of event data recorder. These systems, which are designed and produced by individual motor vehicle manufacturers and component suppliers, are diverse in function, and proprietary in nature. The continuing implementation of EDR systems provides an opportunity to voluntarily standardize the output format of data elements by multiple vehicle manufacturers, which will make MVEDR data more useful to end-users. The recommendations of this SWG will supplement the work of the output SWG by providing a basis for defining output protocols.
File: p1616SWGforData-WorkPlan-draft2.doc

## Slide 9: Objectives
Select Data Elements for inclusion in the IEEE P1616 Data Dictionary.
Develop standard attributes needed for data element specification.
Develop specifications for the output format for each data element.
File: p1616SWGforData-WorkPlan-draft2.doc

## Slide 10: Background
The IEEE P1616 WG is working on a standard for MVEDRs
The data subWG is a sub group of the IEEE WG P1616
EDRs are being manufactured and used in increasing numbers, both as original equipment and aftermarket devices in, for example, race cars.
No standards exist for harmonization of EDRs or the data elements they output
As a result, different EDRs provide data which can not be compared easily
NHTSA sponsored two working groups to review EDRs
  Light vehicle WG
    Developed “top ten” data element list
    Developed “long list” of data elements
  Buses, motorcoaches and trucks WG
    Developed detailed specifications for 28 data elements
    Subdivided them into 3 types: priority 1, 2 and optional
  Finding from these two working groups included lists of data elements, both general and specific
Other groups are (may be) working on standards for EDRs and the WG will need to keep abreast of their activity
File: p1616SWGforData-WorkPlan-draft2.doc

## Slide 11: Deliverables
1b. Work Plan
Presentations to P1616 WG
2. Short Term presentation, Dec 2002
3e. As needed at full P1616 meetings, next Dec 2002
4. Long Term Presentation, TBD
6. Final Product presentation
1f. Compilation of relevant standards and sources of existing data elements
3a. Compilation of candidate MVEDR data element and method for selection of data elements for inclusion in P1616 standard
3c-i. Attributes used to specify data elements
MVEDR Data Definitions Drafts
3d. First Draft
5. Second Draft
6. MVEDR Data Definitions – Final Standard
(numbers correspond to the items in the timeline section).
File: p1616SWGforData-WorkPlan-draft2.doc

## Slide 12: Timeline: Short-Term (Sept. 02)
1a. Recruitment of volunteers.
1b. Prepare a work plan for SWG.
1c. Review existing work on EDRs.
1d. Develop scope, purpose, deliverables, and schedule.
1e. Review existing data bases for data structure.
  1e-i. NASS-CDS
  1e-ii. FARS
  1e-iii. ITS
  1e-iv. Others
1f. Investigate potential sources for data elements.
  1f-i. NHTSA-sponsored EDR WG “top ten” list and other lists developed during this effort
  1f-ii. NHTSA-sponsored T&B EDR WG list of 28
  1f-iii. TMC’s list of data variables
  1f-iv. NTSB’s recommendations
  1f-v. Existing OEM EDR data outputs and existing aftermarket EDRs for race cars, Advanced Crash Notification (ACN) and others.
  1f-vi. SubWG on EDR definition
1g. Investigate and select a sample taxonomy, interrelationships, specific & detailed data definitions.
1h. Investigate language tool(s) and protocols for specification of data element attributes, like “resolution”.
1i. Develop appropriate relationships (e.g., Memorandum-of-Understanding) with other relevant data definition standards activities, like ISO, ITS, SAE.
File: p1616SWGforData-WorkPlan-draft2.doc

## Slide 13: Timeline: September 23, 2002
2. First presentation to IEEE P1616 WG
  2a. Present short-term findings
  2b. Obtain “go-ahead” approval of proposed approach from whole WG
    2b-i. Scope, purpose, deliverables and schedule
    2b-ii. Data dictionary concept
    2b-iii. Taxonomy
    2b-iv. Interrelationships
    2b-v. Data definition approach
  2c. Obtain guidance from P1616 WG on format of final product for inclusion into P1616 document
File: p1616SWGforData-WorkPlan-draft2.doc

## Slide 14: Timeline: Mid-Term (Start Dec. 2002)
3. Long-Term
  3a. Define the EDR data elements for dictionary
    3a-i. Complete review of existing work on EDR data element selection (additional efforts beyond short-term efforts)
    3a-ii. Develop methodology for selecting data elements for dictionary
      3a-ii-1. Possible, each subWG member develop top ten from their various user views and then compile a list
      3a-ii-2. Obtain input from other SubWG
      3a-ii-3. Coordinate with EDR Definition SubWG on stakeholder requests for data element inclusion
    3a-iii. Compile a list of data elements for the data dictionary
      3a-iii-1. Make first cut of variables
      3a-iii-2. Consider priorities for data elements to allow ordering the data definition effort
      3a-iii-3. Set limits for the data definition effort
      3a-iii-4. Complete first cut of data variables
  3b. Develop interrelationships
    3b-i. Decide on approach (possible XML or others)
    3b-ii. Implement approach using first draft of data dictionary
  3c. Develop the definition of each EDR data element
    3c-i. Develop final approach for definition
    3c-ii. Develop definitions for each element in dictionary
    3c-iii. SubWGs’ cross-review of definitions and resolution of differences between stakeholders for common data elements among stakeholders
  3d. Document data dictionary and data definitions in “near-as-possible” final product format
  3e. Update progress of subWG at regularly scheduled P1616 meetings
File: p1616SWGforData-WorkPlan-draft2.doc

## Slide 15: Timeline: Long-Term (2003)
4. Second presentation to IEEE P1616 WG
  4a. Obtain approval of data dictionary
  4b. Obtain approval of each data definition
  4c. Obtain final guidance from P1616 of format of final product
5. Long Term (continued)
  5a. Final updates to data dictionary based on second presentation to P1616
  5b. Final edits of interrelationships
  5c. Final updates/refinements to data definitions
  5d. Final edits of subWG product
6. Deliver final product to P1616 WG.
File: p1616SWGforData-WorkPlan-draft2.doc

## Slide 16: Methods & Materials
Volunteer labor
  Each subWG member will be treated as an individual; not as a representative from their organization (Experience, knowledge, networks, tools).
Work style
  Short term tasks can be executed most efficiently by a group of one.
  Each member works on a specific assignment by himself.
  Present the work result to the subWG for discussion.
  SubWG members will be assigned to execute those short-term tasks.
  If appropriate, task-oriented, sub-subWG could be formed.
Communication
  E-mail
  Telephone, conference calls
  Physical meetings in conjunction with P1616 WG meetings
Materials
  No material costs are anticipated for this effort.
  Labor cost to be donated by volunteers.
File: p1616SWGforData-WorkPlan-draft2.doc

## Slide 17: Objectives vs. SWG Products
1. Selection of Data Elements
  IEEE SCC32 ITS
  SAE J1939
  Hinch Presentation
    NHTSA Truck & Bus EDR Working Group Report
    Aftermarket , ATA-TMC, NHTSA EDR WG, FHWA, NASA-JPL, NHTSA ESV Paper, NTSB, OEM, T&B EDR WG, TRB
  Link between EDR data and Accident Database
2. Selection of Data Attributes
  ITS Data Registry
  SAE J1939
  Language
3. Definition of Data Elements

## Slide 18: Existing Data Definitions: IEEE SCC32
There are already sets of transportation data definitions be IEEE SCC32-SCC32 - Intelligent Transportation Systems. MEVDR Data Definition can be borrowed from them and should be compatible to them.
  1455-1999
    IEEE Standard for Message Sets for Vehicle/Roadside Communications
  1488-2000
    IEEE Trial-Use Standard for Message Set Template for Intelligent Transportation Systems
  1489
    Standard for Data Dictionaries for Intelligent Transportation Systems
  1489
    Standard for Data Dictionaries for Intelligent Transportation Systems RR
  1489-1999
    Standard for Data Dictionaries for Intelligent Transportation Systems
  1512-2000
    IEEE Standard for Common Incident Management Message Sets for use by Emergency Management Centers
  P1512.1
    Standard for Traffic Incident Management Message Sets for Use by Emergency Management Centers
  P1512.2
    Standard for Public Safety Incident Management Message Sets for Use by Emergency Management Centers
  P1512.3
    Standard for Hazardous Material Incident Management Message Sets for Use by Emergency Management Centers
  P1512a
    Standard for Emergency Management Data Dictionary
  1512b
    Amendment for Implementing Foreign Data Elements Found In Standard for Common Incident Management Message Sets For Use By Emergency Management Centers, IEEE 1512-2000
  1512b
    Amendment for Data Elements Found In Standard for Common Incident Management Message Sets For Use By Emergency Management Centers, IEEE 1512- 2000
SCC32ITS.doc

## Slide 19: Existing Data Definitions: SAE Truck & Bus
SAE J1939 for Truck & Bus has more than 15 documents.
  They may be used for EDR data elements definition.
Example of Data Elements from J1939/71 Vehicle Application Layer
  3.2.1.12 Wheel-Base Vehicle Speed
  3.2.1.13 Navigation-Base Vehicle Speed
  3.2.5.9 Road Surface Temperature
  3.2.5.18 Tire Temperature
  3.2.5.30 Brake Application Pressure
  3.2.5.31 Brake Primary Pressure
  3.2.5.34 Tire Pressure
  3.2.5.43 Barometric Pressure
  3.2.5.47 Cruise Control Set Speed
  3.2.5.52 Altitude, Vehicle
  3.2.5.83 Compass Bearing, Vehicle Direction
  3.2.5.84 Pitch, Vehicle
  3.2.5.85 Latitude, Vehicle Position
  3.2.5.86 Longitude, Vehicle Position
  3.2.5.87 VIN, Vehicle Identification Number
  3.2.5.93 Time, Seconds
  3.2.5.94 Time, Minutes
  3.2.5.110 Hours
  3.2.5.111 Day
  3.2.5.112 Year
  3.2.5.113 Month
  Rate / By Request:: 10 sec
  Data Length: 1 bytes
  Resolution, Offset: 4 kpa/bit gain, 0 kpa offset
  Range: 0 to +4000 kpa
  Type: Measured (or Status)

## Slide 20: Existing Data Definitions: NHTSA Truck & Bus EDR Working Group
EDR Data Definitions
  Reference #
  Name
  Acronym
  Other Name
  Definition
  Operation
  Unit of Measure
  Range
  Resolution
  Accuracy
  Sample Rate
  Filter Class
  Discussion
Data Elements
VEHICLE LEVEL
  VEHICLE NUMBER – VEHICLE LEVEL
  NUMBER OF OCCUPANTS
  REGISTRATION STATE
  REGISTERED VEHICLE OWNER
  VEHICLE MAKE, VEHICLE MODEL
  ALPHABETICAL LISTING OF MAKES
  BODY TYPE
  VEHICLE MODEL YEAR
  VEHICLE IDENTIFICATION NUMBER
  BUS USE
  SPECIAL USE
  EMERGENCY USE
  TRAVEL SPEED
  VEHICLE MANEUVER
  CRASH AVOIDANCE MANEUVER
  ROLLOVER
  FIRE OCCURRENCE
  IMPACT POINT – INITIAL/PRINCIPAL
  VEHICLE ROLE
  UNDERRIDE/OVERRIDE
  EXTENT OF DEFORMATION
  MANNER OF LEAVING SCENE
  MOTOR CARRIER IDENTIFICATION NUMBER
  VEHICLE CONFIGURATION
  VEHICLE TRAILING
  NUMBER OF AXLES
  GROSS VEHICLE WEIGHT RATING
  CARGO BODY TYPE
  HAZARDOUS CARGO
  JACKKNIFE
  MOST HARMFUL EVENT
  RELATED FACTORS – VEHICLE LEVEL
File: T&BEDRDataElements.xls

## Slide 21: Existing Data Definitions: NHTSA Truck & Bus EDR Working Group
ACCIDENT LEVEL
  NOTIFICATION TIME EMS
  ARRIVAL TIME EMS
  EMS TIME AT HOSPTIAL
  RELATED FACTORS – ACCIDENT LEVEL
  ADDITIONAL STATE INFORMATION
DRIVER LEVEL:
  VEHICLE NUMBER – DRIVER LEVEL
  DRIVER PRESENCE
  LICENCE STATE
  DRIVER ZIP CODE
  NON-CDL LICENSE STATUS
  COMMERCIAL MOTOR VEHICLE LICENSE STATUS
  COMPLIANCE WITH LICENCE ENDORSEMENTS
  DRIVER LICENSE TYPE COMPLIANCE
  COMPLIANCE WITH LICENSE RESTRICTIONS
  DRIVER HEIGHT
  DRIVER WEIGHT
  DRIVER LEVEL COUNTERS
  DATE OF FIRST AND LAST ACCIDENT,SUSPENSION, CONVICTION
  VIOLATIONS CHARGED
  RELATED FACTORS – DRIVER LEVEL
PERSON LEVEL:
  VEHICLE NUMBER – PERSON LEVEL
  PERSON NUMBER
  NON-MOTORIST STRIKING VEHICLE NUMBER
  AGE
  SEX
  PERSON TYPE
  SEATING POSITION
  RESTRAINT SYSTEM USE
  AIR BAG AVAILABILITY/DEPLOYMENT
  EJECTION
  EJECTION PATH
  EXTRICATION
  NON-MOTORIST LOCATION
  POLICE REPORTED ALCOHOL INVOLVEMENT
  METHOD OF ALCOHOL DETERMINATION BY POLICE
  ALCOHOL TEST TYPE/RESULT
  POLICE – REPORTED OTHER DRUG INVOLVEMENT
  METHOD OF OTHER DRUG DETERMINATION BY POLICE
  DRUG TEST TYPE
  DRUG TEST RESULTS
  INJURY SEVERITY
  TAKEN TO HOSPITAL OR TREATMENT FACILITY
  DIED AT SCENE/EN ROUTE
  DEATH DATE
  DEATH TIME
  RELATED FACTORS – PERSON LEVEL
  DEATH CERTIFICATE NUMBER
  FATAL INJURY AT WORK
  RACE/HISPANIC ORIGIN
File: T&BEDRDataElements.xls

## Slide 22: Selection of Data Elements: Analysis of Accident Database - Summary
Methodology to identify EDR-related data elements in the accident database was developed.
  Step 1: Identify existing accident databases were identified:
    NASS/CDS
      National Automotive Sampling System / Crashworthiness Data System
    NASS/SCI
      National Automotive Sampling System / Special Crash Investigations
    NASS/GES
      National Automotive Sampling System / General Estimates System
    FARS
      Fatality Analysis Reporting System
    HSIS
      Highway Safety Information System
  Step 2: Categorize accident data elements using Modified Haddon Matrix
  Step 3: Categorize EDR data elements using Modified Haddon Matrix
  Step 4: Merge those results to identify the link between EDR & Database
  Example: Apply this method to FARS
Data Elements Characterization Methodology
  IEEE_DataElementCharacterizationMethodology.doc
Fatality Analysis reporting System: Data Element Classification
  IEEE_FARS_Elements_classification.xls

## Slide 23: Selection of Data Elements: Link between EDR Data and Accident Database
EDR Elements for FARS
  Delta-V
  Seat Belt Status
  Time of Day
  VIN
  Vehicle Travel Speed
  (Potential Elements)
  Crash Location
  Crash Related Factors
  Vehicle Maneuver Executed Just Prior to Crash
  Environmental Conditions
  Number of Occupants / Seating Position
  Others
See “Event Data Recorders:
Link with Accident Database,”
September 20, 2002
IEEE_DatabaseLink.ppt

## Slide 24: Data Attributes: ITS Data Registry
“IEEE ITS Data Registry is a centralized data dictionary or repository for all ITS data elements and other data concepts that have been formally specified and established for use with the US national ITS domain.”
  Tom Kurihara is Steward for IEEE (DSRC and NTCIP).
  Attributes are:
    Class Name
    Classification Scheme Name
    Classification Scheme Version
    Data Concept Type
    Relationship Type
    Registration Status
    Representation Class Term
    Submitter Organization Name
    Steward Organization Name
    User
ITSdataRegistry.doc

## Slide 25: Data Attributes: Example from ITS Data Registry – 7.1.2 “Hour”
BASIC META ATTRIBUTES
Descriptive name: HOUR
Descriptive name context: ITS
Definition:
  Sixty minutes, each labeled consecutively in the 24-hour timekeeping system from 0 to 23 beginning with the start of the first minute after the beginning of the hour. Ordinarily, an hour is one twenty-fourth of a day. NOTE: An hour that contains a leap second will have one extra or one second less depending upon whether the leap second is positive or negative, respectively.
Source: ANSI NCITS.310-1998
Class name: ITS
Classification scheme name: IEEE 1489
Classification scheme version: 1.0
Data concept type: Entity
Keyword: hour, time
Related data concept:
Relationship type:
Remarks:
ADMINISTRATIVE META-ATTRIBUTES
Data concept identifier: Auto*
Data concept version: Auto*
Security class: Personal privacy issues.
Registration status: Auto*
Date registered: Auto*
Last change date: Auto*
Last change user: Auto*
Registrar organization: IEEE
Registrar phone number:
Steward organization name: IEEE
Steward phone number:
Submitter organization name: IEEE
Submitter phone number:
User:
View:
Configuration baseline: IEEE Std 1489-1999
Synonymous descriptive name:
Synonymous descriptive name context:
Relevant groups:
Note: “Auto*” should be read as “Automatically input by the data registry.” It is shortened to create space on this slide.
Sample from ITS Data Registry.doc Metaattributes.xls

## Slide 26: Data Attributes: Language
Excel Spread Sheet
  A very good starting point for our work.
XML
  Relationship among data elements.
ASN.1
  A formal description language for use principally to transform application data requirements into encoding schemes that can be sent efficiently across communication lines.

## Slide 27: Reference
E. Garthe and N. Mango
  Technical specifications to permit real time medical use of motor vehicle EDR data to save lives, July 30, 2002
John Hinch
  Data elements presented to IEEE P1616, June 2002
National Automotive Sample System (NASS)
  http://www-nrd.nhtsa.dot.gov/departments/nrd-30/ncsa/AvailInf.html
  Crashworthiness Data System (CDS) Users Analytical Manual 2000
    aman2000.pdf
  CDS Data Collection, Coding and Editing Manual 2000
FARS Electronic 2002 Coding and Validation Manual
  2002manualonly.pdf
FARS Electronic 2001 Coding and Validation Manual,
  2001CodingManual.pdf