## Slide 1: ICAO Threat Model (1)
Encapsulates essential pathologies hypothesized for SV19
  side-to-side asymmetry
  false peaks
  flat top
Consistent with empirical evidence (ringing, edge lag)
Bounded and physically realizable
0
1
2
3
4
5
6
-2.5
-2
-1.5
-1
-0.5
0
0.5
1
1.5
2
2.5
Time (chips)
Normalized amplitude
Code Offset (chips)
Normalized amplitude

1/fd
“Analog” failure component
  Two-pole linear system (LHP)
  Completely described by  and fd

“Digital” failure component
  Delay/advance in falling (or rising) edges only
  Completely described by 

## Slide 2: ICAO Threat Model (2)
Specifies a class of signal anomalies which could lead to hazardously misleading information (HMI)
Implies a dominant error source
(single complex pole pair)
Defines a three-dimensional threat space
  Extensively analyzed by Phelts et. al. (2001)
  Maximum vertical error for a particular correlator spacing and front-end BW is found by exploring this space
Bandwidth (MHz)
Air Spacing (chips)
Notes: In general, GPS satellites are very complicated systems.
The 2OS model is particularly useful in the case where a single physical
mechanism is the dominant source of signal anomaly.
It was adopted by ICAO as a broad description of what might plausibly
go wrong on a satellite. See discussion in Phelts’ dissertation, pp. 41-42
(More complex systems, involving an arbitrary number of poles and zeros,
were considered and rejected for reasons of physical plausibility. Some,
for example, yielded non-causal step responses).
XXX Check with Prof. Enge for how to best word this explanation. XXX

## Slide 3: Vernier Sampling (1)
Given…
  An accurate local oscillator (Rb standard accurate to 1mHz at 10MHz);
  A method to reliably predict Doppler shift of a given satellite as seen from a known location at a given time (demonstrated as part of Oshkosh SV19 analysis);
  A/D converter with sample rate adjustable in fine steps (VSA specified to 1mHz nominally)
What happens when we reduce the sample rate?
Aggregate Epoch
We can increase the effective sample rate by a factor of n over the maximum instrument sample rate
  This occurs at the expense of noise averaging
  Affords improved time resolution provided data set is long enough